## Slide 1: Mercury: A Geo-Aware, mobility-centric messaging system
teja kommineni and kirk webb
Mentor: Kobus van der merwe
Cs6480 project – Fall 2016

## Slide 2: Introduction
Things move around; things with computers attached
  Vehicles: on-board systems, or passenger’s devices
  People: walking, riding bicycles, etc.
  Intelligent Transportation Systems
  Want: location- and trajectory-relevant communication

## Slide 3: introduction
Types of communication
  Road conditions:
    Collisions
    Congestion
    Emergency vehicle
    Unsafe conditions (ice)
  Consumer: gas prices, flash sales, etc.

## Slide 4: Introduction
Message latency requirements
  High (> 1 second)
    Consumer messages
    Congestion, approaching emergency vehicle
  Medium (< 50ms)
    Lane change notification
  Low (< 10ms)
    Immediate control response (collision imminent)

## Slide 5: introduction

## Slide 6: Related work
Focuses on one end or the other
  Vehicle Area Networks
    Clustering, delivery resilience, with LTE bridging
    VMaSC, MDMAC, NHop
  Mobile pubsub
    Tracking changes in association
    MoPS
Deficiencies:
  Little to no attention paid to mobile core network
  No holistic systems (that we could find)

## Slide 7: Enter: mercury
Breaking it down by the tagline:
  A Geo-Aware, Mobility-Centric Messaging System

## Slide 8: Enter: mercury
A Geo-Aware, Mobility-Centric Messaging System
  Location matters. Trajectory matters. Context matters.
  Address endpoints by location (geo-addressing)
  Filter endpoints by context: Area of Interest

## Slide 9: Enter: mercury
A Geo-Aware, Mobility-Centric Messaging System
  The mobility core network is NOT A BLACK BOX!
  Where to deploy components?
  Work with provided mechanisms/facilities
    Broadcasting in 3GPP: eMBMS
    Location-agnostic endpoint addresses (MobilityFirst)

## Slide 10: Enter: mercury
A Geo-Aware, Mobility-Centric Messaging System
  Short, self-contained communication between actors (think: Tweets)
  One message, potentially many clients (pubsub)

## Slide 11: Enter: mercury
A Geo-Aware, Mobility-Centric Messaging System
  An end-to-end message delivery ecosystem
  Can incorporate related work

## Slide 12: Mercury: design goals
Relevant content
  Geo-addressing, context filtering
Robust, low-overhead, low-latency
  Safety messages drive requirements
Flexible deployment
  Existing or new mobile system deployments
Reuse of effective technologies
  PubSub, communication mechanisms (eMBMS)

## Slide 13: Mercury architecture

## Slide 14: Component: pubsub
Apache Kafka, unmodified
Message router
Useful for mobile: offsets

## Slide 15: Component: Broker
Central message processing
Aggregating functions
Data analysis/trending
Not mandatory for comm.

## Slide 16: Component: Adapter
Interface between worlds
Manages client sessions
Uses core network transports
Change for deployment/tech
Enforces Trust

## Slide 17: Component: client endpoint
Client-side interface
Connects local apps
Reports telemetry
Maintains session

## Slide 18: Component: Service endpoint
Centralized processing
In trusted* position
Can use broker
Optional

## Slide 19: Deployment scenarios
Major aspect of the “Flexibility” goal
New deployments
  Metropolitan Intelligent Transportation System
  CloudRAN Data Center
Existing deployments
  Interpose at MTSO (a la SMORE)
  Integrate into eNodeB, right at the edge
  North of PGW, dedicated or default bearer

## Slide 20: Deployment scenarios – Metro ITS

## Slide 21: Deployment scenarios - MTSO

## Slide 22: Deployment scenarios – enodeb