## Slide 1: Mercury: A Geo-Aware, mobility-centric messaging system
teja kommineni and kirk webb
Mentor: Kobus van der merwe
Cs6480 project – Fall 2016

## Slide 2: Introduction
Things move around; things with computers attached
  Vehicles: on-board systems, or passenger’s devices
  People: walking, riding bicycles, etc.
  Intelligent Transportation Systems
  Want: location-relevant communication
  Problem: No holistic mobile messaging system exists…
  Solution: Design and build one!

## Slide 3: Types of messages
  Road conditions:
    Collisions
    Congestion
    Emergency vehicle
    Unsafe conditions (ice)
  Consumer: gas prices, flash sales, etc.

## Slide 4: Message latency requirements
Message latency requirements
  High (> 1 second)
    Consumer messages
    Congestion, approaching emergency vehicle
  Medium (< 50ms)
    Lane change notification
  Low (< 10ms)
    Immediate control response (collision imminent)

## Slide 5: Consequences…

## Slide 6: Our contribution: mercury
  A Geo-Aware, Mobility-Centric Messaging System

## Slide 7: Geo-aware
Location matters. Trajectory matters. Context matters.
Address endpoints by location (geo-addressing)
Filter endpoints by context: Area of Interest

## Slide 8: Mobility-centric
The mobility core network is NOT A BLACK BOX!
Where to deploy components?
Work with provided mechanisms/facilities
  Broadcasting in 3GPP: eMBMS
  Location-agnostic endpoint addresses (MobilityFirst)

## Slide 9: Messaging
Short, self-contained communication between actors (think: Tweets)
One message, potentially many clients (pubsub)

## Slide 10: SysteM
An end-to-end message delivery platform
Can incorporate related work

## Slide 11: Mercury: design goals
Relevant content
  Geo-addressing, context filtering
Robust, low-overhead, low-latency
  Safety messages drive requirements
Flexible deployment
  Existing or new mobile system deployments
Reuse of effective technologies
  PubSub, communication mechanisms (eMBMS)

## Slide 12: Mercury components
Broker
PubSub
Adapter
Service Endpoint
Mobile Core
Access Point
Access Point
Client
Endpoint

## Slide 13: Component: pubsub
Broker
PubSub
Adapter
Service Endpoint
Mobile Core
Access Point
Access Point
Client Endpoint
Apache Kafka, Unmodified
Transports messages by topic
Queue for “going back in time”

## Slide 14: Component: broker
Broker
PubSub
Adapter
Service Endpoint
Mobile Core
Access Point
Access Point
Client Endpoint
Aggregation services (AOI)
Data collection/analysis
Triggers and handlers

## Slide 15: Component: Adapter
Broker
PubSub
Adapter
Service Endpoint
Mobile Core
Access Point
Access Point
Client Endpoint
Interface to Mobile Core
Manages Client Sessions
Client gateway
Scopes Geo-Addresses

## Slide 16: Component: Client endpoint
Broker
PubSub
Adapter
Service Endpoint
Mobile Core
Access Point
Access Point
Client Endpoint
Agent on mobile device
Sends mobile telemetry
Interface for apps

## Slide 17: Component: Service endpoint
Broker
PubSub
Adapter
Service Endpoint
Mobile Core
Access Point
Access Point
Client Endpoint
Service-specific processing
Likely uses Broker services

## Slide 18: Deployment scenarios
Latency/complexity tradeoffs
“Within the City” (future / new) - ~10ms RTT
  Metropolitan Intelligent Transportation System
  CloudRAN Data Center
Existing mobile carrier deployments
  “Tap in” at regional datacenter - ~25ms RTT
  Integrate right at the edge (eNodeB access point) – ~0ms RTT…
  National datacenter at client data egress - ~50ms RTT
Client Endpoint
Mercury in 4G Context

## Slide 19: Related work
Focuses on one end or the other
  Vehicle Area Networks
    Clustering, delivery resilience, with LTE bridging
    VMaSC, MDMAC, NHop
  Mobile pubsub
    Tracking changes in association
    MoPS
Deficiencies:
  Little to no attention paid to mobile core network
  No holistic systems (that we could find)